## Slide 1: Robot Operating System Tutorial ROS Basic
Ling Chen ( lcheno@shu.edu.cn )
From
Shanghai University

## Slide 2: Task and Objective
Learning HOW to use ROS and its tools
  Core concepts of the framework
  Command line tools
  How to write ROS package using Eclipse
  roslaunch

## Slide 3: An Introduction to ROS
What is ROS?
Getting started
ROS file system
ROS graph concepts
Learning by practice

## Slide 4: What is ROS?
hardware abstraction and low-level device control;
Created by California-based Willow Garage, now maintained by the Open Source Robotics Foundation (OSRF);
ROS = plumbing + tools + capabilities + ecosystem.
Notes: plumbing: ROS provides publish-subscribe messaging infrastructure.
tools: ROS provides an extensive set of tools for configuring, starting, introspecting, debugging, visualizing, logging, testing, and stopping distributed computing systems.
capabilities: ROS provides a broad collection of libraries that implement useful robot functionality, with a focus on mobility, manipulation, and perception.
ecosystem: ROS is supported and improved by a large community, with a strong focus on integration and documentation

## Slide 5: What is ROS?
Groovy Galapagos
Fuerte Turtle
Electric
Diamondback
C Turtle
Box Turtle
Hydro
Indigo
Jade

## Slide 6: ROS key features

## Slide 7: ROS key features
hardware abstraction and low-level device control

## Slide 8: ROS key features
hardware abstraction and low-level device control
programming language independence

## Slide 9: ROS key features
hardware abstraction and low-level device control
programming language independence
implementation of a wide range of commonly used tools and algorithms

## Slide 10: ROS key features
hardware abstraction and low-level device control
programming language independence
implementation of a wide range of commonly used tools and algorithms
message passing between processes (OS-independent)

## Slide 11: ROS key features
hardware abstraction and low-level device control
programming language independence
implementation of a wide range of commonly used tools and algorithms
message passing between processes (OS-independent)
standardised package management

## Slide 12: ROS key features
hardware abstraction and low-level device control
programming language independence
implementation of a wide range of commonly used tools and algorithms
message passing between processes (OS-independent)
standardised package management
useful set of shell commands and utilities with tab completion

## Slide 13: ROS concepts and components
ROS client libraries

## Slide 14: ROS concepts and components
Main client libraries:
  Python
  c++
  Lisp
ROS client libraries

## Slide 15: ROS concepts and components
Main client libraries:
  Python
  c++
  Lisp
Experimental client libraries:
  Java (with Android support)
  Lua
ROS client libraries

## Slide 16: Supported operating systems
Supported operating system
    Ubuntu (14.04 LTS + ROS Indigo)
Experimental
Arch
Mac OS X
Debian
OpenSuse
Fedora
Windows
Gentoo

## Slide 17: Supported robots
A lot more on http://www.ros.org/wiki/Robots

## Slide 18: Sensors
1D/2D/3D range finders
  Sharp IR range finder
  Hokuyo laser scanners
  Sick lasers
  Microsoft Kinect
  Asus Xtion

## Slide 19: Sensors
1D/2D/3D range nders
Cameras
  monocular and stereo
  USB (uvc) and rewire
  video streaming (gstreamer)

## Slide 20: Sensors
1D/2D/3D range nders
Cameras
Force/torque/touch sensors
Motion capture systems
Pose estimation (IMU/GPS)
Audio/Speech recognition
RFID
Sensor/actuator interfaces
  Dynamixel
  Phidgets
  Arduino
  Arbotix
  Lego NXT
And many more. . .

## Slide 21: Simulators- Stage

## Slide 22: Simulators- Stage
Stage is a 2D simulator for multiple (large scale) mobile robots

## Slide 23: Simulators- Stage
Stage is a 2D simulator for multiple (large scale) mobile robots
Models for sensors (e.g., laser, sonar) and actuators (e.g., gripper)

## Slide 24: Simulators- Stage
Stage is a 2D simulator for multiple (large scale) mobile robots
Models for sensors (e.g., laser, sonar) and actuators (e.g., gripper)
Models of simple objects for (limited) manipulation

## Slide 25: Simulators- Stage
Stage is a 2D simulator for multiple (large scale) mobile robots
Models for sensors (e.g., laser, sonar) and actuators (e.g., gripper)
Models of simple objects for (limited) manipulation
No physics model at all (e.g., friction, collision, and so forth)

## Slide 26: Simulators- Stage
Stage is a 2D simulator for multiple (large scale) mobile robots
Models for sensors (e.g., laser, sonar) and actuators (e.g., gripper)
Models of simple objects for (limited) manipulation
No physics model at all (e.g., friction, collision, and so forth)
Open source project

## Slide 27: Simulators - Gazebo

## Slide 28: Simulators - Gazebo
Gazebo is a 3D simulator of multiple robots in realistic environments

## Slide 29: Simulators - Gazebo
Gazebo is a 3D simulator of multiple robots in realistic environments
Realistic simulation of rigid body physics/dynamics

## Slide 30: Simulators - Gazebo
Gazebo is a 3D simulator of multiple robots in realistic environments
Realistic simulation of rigid body physics/dynamics
Models for complex robots, actuators and sensors (cameras, IMU)

## Slide 31: Simulators - Gazebo
Gazebo is a 3D simulator of multiple robots in realistic environments
Realistic simulation of rigid body physics/dynamics
Models for complex robots, actuators and sensors (cameras, IMU)
Support provided in part by Open Source Robotics Foundation

## Slide 32: Simulators - Gazebo
Gazebo is a 3D simulator of multiple robots in realistic environments
Realistic simulation of rigid body physics/dynamics
Models for complex robots, actuators and sensors (cameras, IMU)
Support provided in part by Open Source Robotics Foundation
Chosen as the simulator for DARPA (Defense Advanced Research Projects Agency)'s Robot Challenge

## Slide 33: Simulators - Gazebo
Gazebo is a 3D simulator of multiple robots in realistic environments
Realistic simulation of rigid body physics/dynamics
Models for complex robots, actuators and sensors (cameras, IMU)
Support provided in part by Open Source Robotics Foundation
Chosen as the simulator for DARPA (Defense Advanced Research Projects Agency)'s Robot Challenge
Open source project

## Slide 34: Installation - ROS (Indigo) on Ubuntu 14.04 (Trusty )
Setup sources.list
Setup keys
Install ROS Desktop-Full, and standalone tools
Setup environment (shell)
$ sudo sh -c 'echo "deb http://packages.ros.org/ros/ubuntu $(lsb_release -sc) main" > /etc/apt/sources.list.d/ros-latest.list'
$ sudo apt-key adv --keyserver hkp://pool.sks-keyservers.net --recv-key 0xB01FA116
$ sudo apt-get update
$ sudo apt-get install ros-indigo-desktop-full
$ sudo rosdep init
$ rosdep update
$ echo \source /opt/ros/indigo/setup.bash" >> /.bashrc
$. /.bashrc

## Slide 35: Setting up ROS environment for the new user
Type in the following commands
Remember that spaces are necessary, and Linux is case sensitive!
echo ``source /opt/ros/indigo/setup.bash''>>~/.bashrc
source ~/.bashrc
$ mkdir -p ~/catkin_ws/src
$ cd ~/catkin_ws/src
$ catkin_init_workspace
$ cd ~/catkin_ws/
$ catkin_make
$ echo ``source ~/catkin_ws/devel/setup.bash''>>~/.bashrc
$ source ~/.bashrc
echo $ROS_PACKAGE_PATH

## Slide 36: ROS filesystem - Overview
Package
  Meta-packages

## Slide 37: ROS filesystem - Overview
Package
  Packages are the software organization unit of ROS code.
  Meta-packages

## Slide 38: ROS filesystem - Overview
Package
  Packages are the software organization unit of ROS code.
  Each package can contain libraries, executables, scripts, or other artifacts.
  Meta-packages

## Slide 39: ROS filesystem - Overview
Package
  Packages are the software organization unit of ROS code.
  Each package can contain libraries, executables, scripts, or other artifacts.
  Manifest: description (metadata) of a package, whose main role is to define dependencies between packages (package.xml)
  Meta-packages

## Slide 40: ROS filesystem - Overview
Package
  Packages are the software organization unit of ROS code.
  Each package can contain libraries, executables, scripts, or other artifacts.
  Manifest: description (metadata) of a package, whose main role is to define dependencies between packages (package.xml)
  Meta-packages
  Collection of packages forming a higher level library

## Slide 41: ROS filesystem - Overview
Package
  Packages are the software organization unit of ROS code.
  Each package can contain libraries, executables, scripts, or other artifacts.
  Manifest: description (metadata) of a package, whose main role is to define dependencies between packages (package.xml)
  Meta-packages
  Collection of packages forming a higher level library
  Previously called stacks. The concept of stacks was removed with catkin to simplify the growing code base and to support better distribution of packages.

## Slide 42: ROS filesystem – catkin workspace
workspace_folder/ -- WORKSPACE
build/ -- BUILD SPACE CMake is invoked to build the catkin packages in the source space
devel/ -- DEVEL SPACE where built targets are placed prior to being installed
src/ -- SOURCE SPACE
CMakeLists.txt -- 'Toplevel' CMake file, provided by catkin
package_1/
CMakeLists.txt -- CMakeLists.txt file for package_1
package.xml -- Package manifest for package_1
...
package_n/
CMakeLists.txt -- CMakeLists.txt file for package_n
package.xml -- Package manifest for package_n
meta_package/ --collections of packages
sub_package_1/
CMakeLists.txt -- CMakeLists.txt file for sub_package_1
package.xml -- Package manifest for sub_package_1
…
sub_package_n/
CMakeLists.txt -- CMakeLists.txt file for sub_package_n
package.xml -- Package manifest for sub_package_n
meta_package/
package.xml -- Package manifest indicating the meta_package

## Slide 43
ROS filesystem – Package Example
Hypothetical package myPkg/

## Slide 44
CMakeLists.txt: CMake build settings for package myPkg
ROS filesystem – Package Example
Hypothetical package myPkg/

## Slide 45
CMakeLists.txt: CMake build settings for package myPkg
package.xml: metadata and dependencies required by package
ROS filesystem – Package Example
Hypothetical package myPkg/

## Slide 46
CMakeLists.txt: CMake build settings for package myPkg
package.xml: metadata and dependencies required by package
mainpage.dox: doc information of package myPkg
ROS filesystem – Package Example
Hypothetical package myPkg/

## Slide 47
CMakeLists.txt: CMake build settings for package myPkg
package.xml: metadata and dependencies required by package
mainpage.dox: doc information of package myPkg
include/myPkg: c++ header files
ROS filesystem – Package Example
Hypothetical package myPkg/

## Slide 48
CMakeLists.txt: CMake build settings for package myPkg
package.xml: metadata and dependencies required by package
mainpage.dox: doc information of package myPkg
include/myPkg: c++ header files
src/: source code directory
ROS filesystem – Package Example
Hypothetical package myPkg/

## Slide 49
CMakeLists.txt: CMake build settings for package myPkg
package.xml: metadata and dependencies required by package
mainpage.dox: doc information of package myPkg
include/myPkg: c++ header files
src/: source code directory
launch/: where launch files are stored (if needed)
ROS filesystem – Package Example
Hypothetical package myPkg/

## Slide 50
CMakeLists.txt: CMake build settings for package myPkg
package.xml: metadata and dependencies required by package
mainpage.dox: doc information of package myPkg
include/myPkg: c++ header files
src/: source code directory
launch/: where launch files are stored (if needed)
msg/: message (.msg) types
ROS filesystem – Package Example
Hypothetical package myPkg/

## Slide 51
CMakeLists.txt: CMake build settings for package myPkg
package.xml: metadata and dependencies required by package
mainpage.dox: doc information of package myPkg
include/myPkg: c++ header files
src/: source code directory
launch/: where launch files are stored (if needed)
msg/: message (.msg) types
srv/: service (.srv) types
ROS filesystem – Package Example
Hypothetical package myPkg/

## Slide 52
CMakeLists.txt: CMake build settings for package myPkg
package.xml: metadata and dependencies required by package
mainpage.dox: doc information of package myPkg
include/myPkg: c++ header files
src/: source code directory
launch/: where launch files are stored (if needed)
msg/: message (.msg) types
srv/: service (.srv) types
scripts/: executable scripts
ROS filesystem – Package Example
Hypothetical package myPkg/

## Slide 53: rosbash -ROS command line tools
Open up a terminal
  Press \windows" key, then type \terminal", then press \Enter or use shortcut Ctrl+Alt+T

## Slide 54: rosbash -ROS command line tools

## Slide 55: rosbash -ROS command line tools
rospack: ROS package management tool

## Slide 56: rosbash -ROS command line tools
rospack: ROS package management tool
  $ rospack list
  $ rospack find turtlesim
  $ rospack depends turtlesim
  $ rospack profile

## Slide 57: rosbash -ROS command line tools
rospack: ROS package management tool
roscd: change directory command for ROS
  $ rospack list
  $ rospack find turtlesim
  $ rospack depends turtlesim
  $ rospack profile

## Slide 58: rosbash -ROS command line tools
rospack: ROS package management tool
roscd: change directory command for ROS
  $ rospack list
  $ rospack find turtlesim
  $ rospack depends turtlesim
  $ rospack profile
  $ roscd
  $ roscd turtlesim
  $ ls (standard linux shell command)

## Slide 59: rosbash -ROS command line tools
rospack: ROS package management tool
roscd: change directory command for ROS
rosls: allows you to list the contents of a ROS package
  $ rospack list
  $ rospack find turtlesim
  $ rospack depends turtlesim
  $ rospack profile
  $ roscd
  $ roscd turtlesim
  $ ls (standard linux shell command)

## Slide 60: rosbash -ROS command line tools
rospack: ROS package management tool
roscd: change directory command for ROS
rosls: allows you to list the contents of a ROS package
  $ rospack list
  $ rospack find turtlesim
  $ rospack depends turtlesim
  $ rospack profile
  $ roscd (return to workspace directory)
  $ rosls turtlesim
  $ roscd
  $ roscd turtlesim
  $ ls (standard linux shell command)

## Slide 61: Nodes
control robot wheel motors
acquire data from laser scanner
acquire images from camera
perform localisation
perform path planning
provide graphical visualisation of the system
Nodes are processes which perform specific computations:

## Slide 62: Master

## Slide 63: Master
Master is the core node of ROS, called roscore

## Slide 64: Master
Master is the core node of ROS, called roscore
Acts as a nameservice for the Computation Graph

## Slide 65: Master
Master is the core node of ROS, called roscore
Acts as a nameservice for the Computation Graph
Stores topics and services registration information for ROS nodes

## Slide 66: Master
Master is the core node of ROS, called roscore
Acts as a nameservice for the Computation Graph
Stores topics and services registration information for ROS nodes
Nodes then establish connections as appropriate

## Slide 67: Master
Master is the core node of ROS, called roscore
Acts as a nameservice for the Computation Graph
Stores topics and services registration information for ROS nodes
Nodes then establish connections as appropriate
Also makes callbacks to nodes when registration information changes

## Slide 68: Master
Master is the core node of ROS, called roscore
Acts as a nameservice for the Computation Graph
Stores topics and services registration information for ROS nodes
Nodes then establish connections as appropriate
Also makes callbacks to nodes when registration information changes
Allows nodes to dynamically create connections as new nodes are run

## Slide 69: Parameter server

## Slide 70: Parameter server
Open up a terminal, then run ROS Master node

## Slide 71: Parameter server
Open up a terminal, then run ROS Master node
  $ roscore

## Slide 72: Parameter server
Open up a terminal, then run ROS Master node
In another terminal, explore the parameter server
  $ roscore

## Slide 73: Parameter server
Open up a terminal, then run ROS Master node
In another terminal, explore the parameter server
  $ roscore
  $ rosparam list
  $ rosparam get /rosdistro
  $ rosparam get /rosversion

## Slide 74: Parameter server
Open up a terminal, then run ROS Master node
In another terminal, explore the parameter server
It should look like this
  $ roscore
  $ rosparam list
  $ rosparam get /rosdistro
  $ rosparam get /rosversion

## Slide 75: Parameter server
Open up a terminal, then run ROS Master node
In another terminal, explore the parameter server
It should look like this
  $ roscore
  $ rosparam list
  $ rosparam get /rosdistro
  $ rosparam get /rosversion

## Slide 76: Messages

## Slide 77: Messages
Messages are simply a data structure, consisting of typed fields

## Slide 78: Messages
Messages are simply a data structure, consisting of typed fields
Standard primitive types (and nested arrays) are supported:
  int8, 16, 32, 64
  float32, 64
  string
  time
  duration
  array[]
  For more information, go to http://wiki.ros.org/msg

## Slide 79: Messages
Messages are simply a data structure, consisting of typed fields
Standard primitive types (and nested arrays) are supported:
  int8, 16, 32, 64
  float32, 64
  string
  time
  duration
  array[]
  For more information, go to http://wiki.ros.org/msg
Nodes communicate with each other by passing messages

## Slide 80: Messages
Messages are simply a data structure, consisting of typed fields
Standard primitive types (and nested arrays) are supported:
  int8, 16, 32, 64
  float32, 64
  string
  time
  duration
  array[]
  For more information, go to http://wiki.ros.org/msg
Nodes communicate with each other by passing messages
Routed via a transport system with publish/subscribe semantics

## Slide 81: Messages
Messages are simply a data structure, consisting of typed fields
Standard primitive types (and nested arrays) are supported:
  int8, 16, 32, 64
  float32, 64
  string
  time
  duration
  array[]
  For more information, go to http://wiki.ros.org/msg
Nodes communicate with each other by passing messages
Routed via a transport system with publish/subscribe semantics
When used with topics: *.msg (n:n)

## Slide 82: Messages
Messages are simply a data structure, consisting of typed fields
Standard primitive types (and nested arrays) are supported:
  int8, 16, 32, 64
  float32, 64
  string
  time
  duration
  array[]
  For more information, go to http://wiki.ros.org/msg
Nodes communicate with each other by passing messages
Routed via a transport system with publish/subscribe semantics
When used with topics: *.msg (n:n)
When used with services: *.srv (1:1 { request + response})

## Slide 83: Topics

## Slide 84: Topics
A node sends out a message by publishing it to a given Topic

## Slide 85: Topics
A node sends out a message by publishing it to a given Topic
The topic type is defined by the message type publishing on it

## Slide 86: Topics
A node sends out a message by publishing it to a given Topic
The topic type is defined by the message type publishing on it
A node requiring a certain type of data must subscribe to the
appropriate Topic

## Slide 87: Topics
A node sends out a message by publishing it to a given Topic
The topic type is defined by the message type publishing on it
A node requiring a certain type of data must subscribe to the
appropriate Topic
Multiple publishers/subscribers to the same Topic are allowed

## Slide 88: Topics
A node sends out a message by publishing it to a given Topic
The topic type is defined by the message type publishing on it
A node requiring a certain type of data must subscribe to the
appropriate Topic
Multiple publishers/subscribers to the same Topic are allowed
A single node may publish and/or subscribe to multiple Topics

## Slide 89: Topics
A node sends out a message by publishing it to a given Topic
The topic type is defined by the message type publishing on it
A node requiring a certain type of data must subscribe to the
appropriate Topic
Multiple publishers/subscribers to the same Topic are allowed
A single node may publish and/or subscribe to multiple Topics
Publishers and subscribers are generally unaware of each other's
existence

## Slide 90: Topics
A node sends out a message by publishing it to a given Topic
The topic type is defined by the message type publishing on it
A node requiring a certain type of data must subscribe to the
appropriate Topic
Multiple publishers/subscribers to the same Topic are allowed
A single node may publish and/or subscribe to multiple Topics
Publishers and subscribers are generally unaware of each other's
existence
Publish/subscribe model is a flexible paradigm (many-to-many,
one-way transport)

## Slide 91: Topics
A node sends out a message by publishing it to a given Topic
The topic type is defined by the message type publishing on it
A node requiring a certain type of data must subscribe to the
appropriate Topic
Multiple publishers/subscribers to the same Topic are allowed
A single node may publish and/or subscribe to multiple Topics
Publishers and subscribers are generally unaware of each other's
existence
Publish/subscribe model is a flexible paradigm (many-to-many,
one-way transport)
There is no order of execution required

## Slide 92: Topics -diagrammatic representation
Xml/RPC: http://en.wikipedia.org/wiki/XML-RPC

## Slide 93: Services

## Slide 94: Services
Publish/subscribe paradigm not appropriate for services

## Slide 95: Services
Publish/subscribe paradigm not appropriate for services
Services implement the request/reply functionality

## Slide 96: Services
Publish/subscribe paradigm not appropriate for services
Services implement the request/reply functionality
Pair of message structures: one for request and one for reply

## Slide 97: Services
Publish/subscribe paradigm not appropriate for services
Services implement the request/reply functionality
Pair of message structures: one for request and one for reply
A node provider offers a service under a specific name

## Slide 98: Services
Publish/subscribe paradigm not appropriate for services
Services implement the request/reply functionality
Pair of message structures: one for request and one for reply
A node provider offers a service under a specific name
A client node uses the service by sending the request message and awaits for the reply

## Slide 99: Services
Publish/subscribe paradigm not appropriate for services
Services implement the request/reply functionality
Pair of message structures: one for request and one for reply
A node provider offers a service under a specific name
A client node uses the service by sending the request message and awaits for the reply
From the programmer perspective, works as a remote procedure call

## Slide 100: Services - diagrammatic representation

## Slide 101: Messages-more ROS command line goodies

## Slide 102
Message over Topics
Messages-more ROS command line goodies

## Slide 103: Messages-more ROS command line goodies
Message over Topics
  $ rosmsg list
  $ rosmsg show geomemtry_msgs/Vector3
  $ rosmsg show geomemtry_msgs/Twist

## Slide 104: Messages-more ROS command line goodies
Message over Topics
Vector3.msg and Twist.msg from package geometry_msgs
  $ rosmsg list
  $ rosmsg show geomemtry_msgs/Vector3
  $ rosmsg show geomemtry_msgs/Twist

## Slide 105: Messages-more ROS command line goodies
Message over Topics
Vector3.msg and Twist.msg from package geometry_msgs
  $ rosmsg list
  $ rosmsg show geomemtry_msgs/Vector3
  $ rosmsg show geomemtry_msgs/Twist

## Slide 106
Messages-more ROS command line goodies

## Slide 107: Messages-more ROS command line goodies
Message over Services

## Slide 108: Messages-more ROS command line goodies
Message over Services
  $ rossrv list
  $ rossrv show turtlesim/Spawn

## Slide 109: Messages-more ROS command line goodies
Message over Services
Spawn.msg from package geometry
  $ rossrv list
  $ rossrv show turtlesim/Spawn

## Slide 110: Messages-more ROS command line goodies
Message over Services
Spawn.msg from package geometry
  $ rossrv list
  $ rossrv show turtlesim/Spawn

## Slide 111: roscore

## Slide 112: roscore
roscore
  roscore is a collection of nodes and programs that are pre-requisites of a ROS-based system. You must have a roscore running in order for ROS nodes to communicate. It is launched using the roscore command.

## Slide 113: roscore
roscore
  roscore is a collection of nodes and programs that are pre-requisites of a ROS-based system. You must have a roscore running in order for ROS nodes to communicate. It is launched using the roscore command.

## Slide 114: rosrun

## Slide 115: rosrun
rosrun allows to run an executable in arbitrary package without knowing its location

## Slide 116: rosrun
rosrun allows to run an executable in arbitrary package without knowing its location
rosrun package executable
Example: rosrun cmd_vel_publisher cmd_vel_publisher_node

## Slide 117: rosrun
rosrun allows to run an executable in arbitrary package without knowing its location
rosrun package executable
It's also possible to pass parameters
Example: rosrun cmd_vel_publisher cmd_vel_publisher_node

## Slide 118: rosrun
rosrun allows to run an executable in arbitrary package without knowing its location
rosrun package executable
It's also possible to pass parameters
rosrun package node _parameter:=value
Example:
rosrun cmd_vel_publisher cmd_vel_publisher_node _Max_Constant_Vel:=0.5
Example: rosrun cmd_vel_publisher cmd_vel_publisher_node

## Slide 119: Practice with rosrun

## Slide 120: Practice with rosrun
rosrun with turtlesim_node

## Slide 121: Practice with rosrun
rosrun with turtlesim_node
$ rosrun turtlesim turtlesim_node

## Slide 122: Practice with rosrun

## Slide 123: Practice with rosrun
rosrun with turtlesim_teleop_key
Using the arrow keys to drive the robot

## Slide 124: Practice with rosrun
rosrun with turtlesim_teleop_key
Using the arrow keys to drive the robot
$ rosrun turtlesim turtle_teleop_key

## Slide 125: rosnode
The current list of supported commands are

## Slide 126: rosnode
The current list of supported commands are
  rosnode kill kill a running node

## Slide 127: rosnode
The current list of supported commands are
  rosnode kill kill a running node
  rosnode list list active nodes

## Slide 128: rosnode
The current list of supported commands are
  rosnode kill kill a running node
  rosnode list list active nodes
  rosnode machine list nodes running on a machines

## Slide 129: rosnode
The current list of supported commands are
  rosnode kill kill a running node
  rosnode list list active nodes
  rosnode machine list nodes running on a machines
  rosnode ping test connectivity to node

## Slide 130: rosnode
The current list of supported commands are
  rosnode kill kill a running node
  rosnode list list active nodes
  rosnode machine list nodes running on a machines
  rosnode ping test connectivity to node
  rosnode info print information about node

## Slide 131: rostopic
The current list of supported commands are

## Slide 132: rostopic
The current list of supported commands are
  rostopic bw display bandwidth used by topic

## Slide 133: rostopic
The current list of supported commands are
  rostopic bw display bandwidth used by topic
  rostopic echo print messages to screen

## Slide 134: rostopic
The current list of supported commands are
  rostopic bw display bandwidth used by topic
  rostopic echo print messages to screen
  rostopic find find topics by type

## Slide 135: rostopic
The current list of supported commands are
  rostopic bw display bandwidth used by topic
  rostopic echo print messages to screen
  rostopic find find topics by type
  rostopic hz display publishing rate of topic

## Slide 136: rostopic
The current list of supported commands are
  rostopic bw display bandwidth used by topic
  rostopic echo print messages to screen
  rostopic find find topics by type
  rostopic hz display publishing rate of topic
  rostopic info print information about active topic

## Slide 137: rostopic
The current list of supported commands are
  rostopic bw display bandwidth used by topic
  rostopic echo print messages to screen
  rostopic find find topics by type
  rostopic hz display publishing rate of topic
  rostopic info print information about active topic
  rostopic list print informaion about active topics

## Slide 138: rostopic
The current list of supported commands are
  rostopic bw display bandwidth used by topic
  rostopic echo print messages to screen
  rostopic find find topics by type
  rostopic hz display publishing rate of topic
  rostopic info print information about active topic
  rostopic list print informaion about active topics
  rostopic pub publish data to topic

## Slide 139: rostopic

## Slide 140: rostopic
rostopic pub
$ rostopic pub [topic] [msg_type] [arg]

## Slide 141: rostopic
rostopic pub
$ rostopic pub [topic] [msg_type] [arg]
rostopic pub /turtle1/cmd_vel geometry_msgs/Twist -r 1 -- '[2.0, 0.0, 0.0]' '[0.0, 0.0, 1.8]'

## Slide 142: ROS Development Procedures
Create a new catkin workspace
Create a new ROS package
Download and configure Eclipse
Create Eclipse project file for your package
Import package into Eclipse
Write the code
Update the make file
Build the package

## Slide 143: catkin Workspace
A workspace is a directory in which one or more catkin packages can be built.
A basic workspace looks like this:
workspace_folder/ -- WORKSPACE
build/ -- BUILD SPACE CMake is invoked to build the catkin packages in the source space
devel/ -- DEVEL SPACE where built targets are placed prior to being installed
src/ -- SOURCE SPACE
CMakeLists.txt -- 'Toplevel' CMake file, provided by catkin
package_1/
CMakeLists.txt -- CMakeLists.txt file for package_1
package.xml -- Package manifest for package_1
...
package_n/
CMakeLists.txt -- CMakeLists.txt file for package_n
package.xml -- Package manifest for package_n
meta_package/ --collections of packages
sub_package_1/
CMakeLists.txt -- CMakeLists.txt file for sub_package_1
package.xml -- Package manifest for sub_package_1
…
sub_package_n/
CMakeLists.txt -- CMakeLists.txt file for sub_package_n
package.xml -- Package manifest for sub_package_n
meta_package/
package.xml -- Package manifest indicating the meta_package

## Slide 144: Creating a catkin Workspace
http://wiki.ros.org/catkin/Tutorials/create_a_workspace
Initially, the workspace will contain only the top-level CMakeLists.txt
catkin_make command builds the workspace and all the packages within it
$ mkdir -p ~/catkin_ws/src
$ cd ~/catkin_ws/src
$ catkin_init_workspace
cd ~/catkin_ws
catkin_make

## Slide 145: Resulting catkin Workspace
The resulting build artifacts and executables are placed into the devel space

## Slide 146: The Package Manifest
XML file that defines properties about the package such as:
  the package name
  version numbers
  authors
  dependencies on other catkin packages

## Slide 147: The Package Manifest
Example for a package manifest:

## Slide 148: Creating a ROS Package
http://wiki.ros.org/catkin/Tutorials/CreatingPackage
Change to the source directory of the workspace
catkin_create_pkg creates a new package
Example:
  $ catkin_create_pkg <package_name> [depend1] [depend2] [depend3]
  $ catkin_create_pkg test_package std_msgs rospy roscpp
  $cd ~/catkin_ws/src

## Slide 149: ROS IDEs
http://wiki.ros.org/IDEs
For building and running ROS programs from IDEs, the ROS environment has to be set up.
  Running your IDE from your ROS-sourced shell should be the easiest way
  Likewise, you can enhance your IDE's launcher icon to load your shells environment.

## Slide 150: Installing Eclipse- Installing JDK
Download JDK 7 to ~/Downloads via:
http://yunpan.cn/cwU9iUq9iz9KD Password: fccc
Extract it:
Move the extracted folder to /usr/lib/jvm
Create a file /etc/profile.d/oraclejdk.sh with the following content (adapt the paths to reflect the path where you stored your JDK):
  $ tar -xf jdk-7u79-linux-x64.gz
  export J2SDKDIR=/usr/lib/jvm/oracle_jdk7
  export J2REDIR=/usr/lib/jvm/oracle_jdk7/jre
  export PATH=$PATH:/usr/lib/jvm/oracle_jdk7/bin:/usr/lib/jvm/oracle_jdk7/db/bin:/usr/lib/jvm/oracle_jdk7/jre/bin
  export JAVA_HOME=/usr/lib/jvm/oracle_jdk7
  export DERBY_HOME=/usr/lib/jvm/oracle_jdk7/db
  $ sudo mv /home/viki/Downloads/jdk1.7.0_79 /usr/lib/jvm/oracle_jdk7

## Slide 151: Installing Eclipse
Download eclipse IDE for C/C++ developers from http://www.eclipse.org/downloads/
  Latest version of the file is: eclipse-cpp-luna-SR2-linux-gtk-x86_64.tar.gz
Extract eclipse into a folder of your choice
Move eclipse to the /opt folder.
Create a link to it so it can be used by all users
  $ sudo mv eclipse /opt
  $ sudo ln -s /opt/eclipse/eclipse /usr/bin/eclipse

## Slide 152: Installing Eclipse
Make an entry in the Unity Dash for easier access
  The bash -i -c command will cause your IDE's launcher icon to load your ROS-sourced shell environment before launching eclipse
[Desktop Entry]
Name=Eclipse
Type=Application
Exec=bash -i -c "/opt/eclipse/eclipse"
Terminal=false
Icon=/opt/eclipse/icon.xpm
Comment=Integrated Development Environment
NoDisplay=false
Categories=Development;IDE
Name[en]=eclipse.desktop
  $sudo gedit /usr/share/applications/eclipse.desktop

## Slide 153: Learning by Practice
How to customize your own message and service
How to publish a topic
How to subscribe a topic
How to build a server
How to build a client

## Slide 154: Learning by Practice
How to customize your own message and service
How to publish a topic
How to subscribe a topic
How to build a server
How to build a client

## Slide 155: Creating your own package

## Slide 156: Creating your own package
Create a new package

## Slide 157: Creating your own package
Create a new package
cd ~/catkin_ws/src
catkin_create_pkg beginner_tutorials std_msgs rospy roscpp

## Slide 158: Creating your own package

## Slide 159: Creating your own package
Make two folders for messages and services

## Slide 160: Creating your own package
Make two folders for messages and services
$ roscd beginner_tutorials
$ mkdir msg
$ mkdir srv

## Slide 161: Creating your own package
Make two folders for messages and services
In msg, create a file called AandB.msg, with content:
  float32 a
  float32 b
$ roscd beginner_tutorials
$ mkdir msg
$ mkdir srv

## Slide 162: Creating your own package
Make two folders for messages and services
In msg, create a file called AandB.msg, with content:
  float32 a
  float32 b
In srv, create a file called AddTwoInts.srv, with content:
  int64 A
  int64 B
  ---
  int64 Sum
$ roscd beginner_tutorials
$ mkdir msg
$ mkdir srv

## Slide 163: Modify Package.xml and CMakeLists.txt

## Slide 164: Modify Package.xml and CMakeLists.txt
Change package.xml.
Open package.xml, and make sure these two lines are in it and uncommented:
<build_depend>message_generation</build_depend>
<run_depend>message_runtime</run_depend>

## Slide 165: Modify Package.xml and CMakeLists.txt
Change package.xml.
Open package.xml, and make sure these two lines are in it and uncommented:
<build_depend>message_generation</build_depend>
<run_depend>message_runtime</run_depend>
Add message_generation dependency in CMakeLists.txt.
find_package(catkin REQUIRED COMPONENTS roscpp rospy
std_msgs message_generation)

## Slide 166: Modify Package.xml and CMakeLists.txt
Change package.xml.
Open package.xml, and make sure these two lines are in it and uncommented:
<build_depend>message_generation</build_depend>
<run_depend>message_runtime</run_depend>
Add message_generation dependency in CMakelists.txt.
find_package(catkin REQUIRED COMPONENTS roscpp rospy
std_msgs message_generation)
Also make sure you export the message runtime dependency.
catkin_package(
...
CATKIN_DEPENDS message_runtime ...)

## Slide 167: Modify Package.xml and CMakeLists.txt

## Slide 168: Modify Package.xml and CMakeLists.txt
Change CMakelists.txt.
Find the following block of code:
# add_message_files(
# FILES
# Message1.msg
# Message2.msg
# )
Uncomment it by removing the # symbols and change to this: add_message_files( FILES AandB.msg )

## Slide 169: Modify Package.xml and CMakeLists.txt
Change CMakelists.txt.
Find the following block of code:
# add_message_files(
# FILES
# Message1.msg
# Message2.msg
# )
Uncomment it by removing the # symbols and change to this: add_message_files( FILES AandB.msg )
Remove # to uncomment the following lines:
# add_service_files(
# FILES
# Service1.srv
# Service2.srv
# )
And replace the placeholder Service*.srv files for your service files:
add_service_files( FILES AddTwoInts.srv)

## Slide 170: Modify Package.xml and CMakeLists.txt
package.xml should look like:
<?xml version="1.0"?>
<package>
<name>beginner_tutorials</name>
<version>0.0.0</version>
<description>The beginner_tutorials package</description>
<maintainer email="ling@todo.todo">ling</maintainer>
<license>TODO</license>
<build_depend>message_generation</build_depend>
<buildtool_depend>catkin</buildtool_depend>
<run_depend>message_runtime</run_depend>
<buildtool_depend>catkin</buildtool_depend>
<build_depend>roscpp</build_depend>
<build_depend>rospy</build_depend>
<build_depend>std_msgs</build_depend>
<run_depend>roscpp</run_depend>
<run_depend>rospy</run_depend>
<run_depend>std_msgs</run_depend>
<export>
</export>
</package>

## Slide 171: Modify Package.xml and CMakeLists.txt
CMakeLists.txt should look like:
cmake_minimum_required(VERSION 2.8.3)
project(beginner_tutorials)
find_package(catkin REQUIRED COMPONENTS
roscpp
rospy
std_msgs
message_generation
)
add_message_files( FILES AandB.msg )
add_service_files ( FILES AddTwoInts.srv )
generate_messages( DEPENDENCIES std_msgs )
catkin_package( CATKIN_DEPENDS roscpp rospy std_msgs message_runtime )
include_directories( ${catkin_INCLUDE_DIRS} )

## Slide 172: Make Eclipse Project Files
Go to workspace directory and run catkin_make with options to generate eclipse project files:
The project files will be generated in the build/ folder (~/catkin_ws/build/.project and ~/catkin_ws/build/.cproject)
  $cd ~/catkin_ws
  $catkin_make --force-cmake -G"Eclipse CDT4 - Unix Makefiles"

## Slide 173: Import the Project into Eclipse
Now start Eclipse
Choose catkin_ws folder as the workspace folder

## Slide 174: Import the Project into Eclipse
Choose File --> Import --> General --> Existing Projects into Workspace

## Slide 175: Import the Project into Eclipse
Now import the project from the ~/catkin_ws/build folder

## Slide 176: Fix Preprocessor Include Paths
By default, the intellisense in Eclipse won’t recognize the system header files (like <string>). To fix that:
  Go to Project Properties --> C/C++ General --> Preprocessor Include Paths, Macros, etc. --> Providers tab
  Check CDT GCC Built-in Compiler Settings

## Slide 177: Fix Preprocessor Include Paths
After that rebuild the C/C++ index by Right click on project -> Index -> Rebuild

## Slide 178: Project Structure
Eclipse provides a link "Source directory" within the project so that you can edit the source code

## Slide 179: Learning by Practice
How to customize your own message and service
How to publish a topic
How to subscribe a topic
How to build a server
How to build a client

## Slide 180: Add New Source File
Right click on src and select New –> Source File, and create a file named talker.cpp

## Slide 181: Code Completion
Use Eclipse standard shortcuts to get code completion (i.e., Ctrl+Space)

## Slide 182: ROS C++ Client Library
roscpp is a ROS client implementation in C++
Library documentation can be found at:
  http://docs.ros.org/api/roscpp/html/
ROS header files can be found at: /opt/ros/hydro/include
  For example, /opt/ros/hydro/include/ros/ros.h
ROS core binaries are located at: /opt/ros/hydro/bin
  For example, /opt/ros/hydro/bin/rosrun

## Slide 183: ROS Init
A version of ros::init() must be called before using any of the rest of the ROS system

## Slide 184: ROS Init
A version of ros::init() must be called before using any of the rest of the ROS system
Typical call in the main() function:

## Slide 185: ROS Init
A version of ros::init() must be called before using any of the rest of the ROS system
Typical call in the main() function:
  ros::init(argc, argv, “Node name”);

## Slide 186: ROS Init
A version of ros::init() must be called before using any of the rest of the ROS system
Typical call in the main() function:
Node names must be unique in a running system
  ros::init(argc, argv, “Node name”);

## Slide 187: ros::NodeHandle

## Slide 188: ros::NodeHandle
The main access point to communications with the ROS system.
  Provides public interface to topics, services, parameters, etc.

## Slide 189: ros::NodeHandle
The main access point to communications with the ROS system.
  Provides public interface to topics, services, parameters, etc.
Create a handle to this process’ node (after the call to ros::init()) by declaring:

## Slide 190: ros::NodeHandle
The main access point to communications with the ROS system.
  Provides public interface to topics, services, parameters, etc.
Create a handle to this process’ node (after the call to ros::init()) by declaring:
  ros::NodeHandle n;

## Slide 191: ros::NodeHandle
The main access point to communications with the ROS system.
  Provides public interface to topics, services, parameters, etc.
Create a handle to this process’ node (after the call to ros::init()) by declaring:
  The first NodeHandle constructed will fully initialize the current node
  The last NodeHandle destructed will close down the node
  ros::NodeHandle n;

## Slide 192: ros::Publisher

## Slide 193: ros::Publisher
Manages an advertisement on a specific topic.

## Slide 194: ros::Publisher
Manages an advertisement on a specific topic.
A Publisher is created by calling NodeHandle::advertise()
  Registers this topic in the master node

## Slide 195: ros::Publisher
Manages an advertisement on a specific topic.
A Publisher is created by calling NodeHandle::advertise()
  Registers this topic in the master node
Example for creating a publisher:

## Slide 196: ros::Publisher
Manages an advertisement on a specific topic.
A Publisher is created by calling NodeHandle::advertise()
  Registers this topic in the master node
Example for creating a publisher:
  ros::Publisher chatter_pub = n.advertise<std_msgs::String>("chatter", 1000);

## Slide 197: ros::Publisher
Manages an advertisement on a specific topic.
A Publisher is created by calling NodeHandle::advertise()
  Registers this topic in the master node
Example for creating a publisher:
  First parameter is the topic name
  Second parameter is the queue size
  ros::Publisher chatter_pub = n.advertise<std_msgs::String>("chatter", 1000);

## Slide 198: ros::Publisher
Manages an advertisement on a specific topic.
A Publisher is created by calling NodeHandle::advertise()
  Registers this topic in the master node
Example for creating a publisher:
  First parameter is the topic name
  Second parameter is the queue size
Once all Publishers for a given topic go out of scope the topic will be unadvertised
  ros::Publisher chatter_pub = n.advertise<std_msgs::String>("chatter", 1000);

## Slide 199: ros::Publisher

## Slide 200: ros::Publisher
Messages are published on a topic through a call to publish()

## Slide 201: ros::Publisher
Messages are published on a topic through a call to publish()
Example:

## Slide 202: ros::Publisher
Messages are published on a topic through a call to publish()
Example:
  std_msgs::String msg;
  chatter_pub.publish(msg);

## Slide 203: ros::Publisher
Messages are published on a topic through a call to publish()
Example:
The type of the message object must agree with the type given as a template parameter to the advertise<>() call
  std_msgs::String msg;
  chatter_pub.publish(msg);

## Slide 204: ros::Rate
A class to help run loops at a desired frequency.
Specify in the constructor the desired rate to run in Hz
ros::Rate::sleep() method
  Sleeps for any leftover time in a cycle.
  Calculated from the last time sleep, reset, or the constructor was called
  ros::Rate loop_rate(10);

## Slide 205: ros::ok()

## Slide 206: ros::ok()
Call ros::ok() to check if the node should continue running

## Slide 207: ros::ok()
Call ros::ok() to check if the node should continue running
ros::ok() will return false if:
  a SIGINT is received (Ctrl-C)
  we have been kicked off the network by another node with the same name
  ros::shutdown() has been called by another part of the application.
  all ros::NodeHandles have been destroyed

## Slide 208: C++ Publisher Node Example talker.cpp
#include "ros/ros.h"
#include "beginner_tutorials/AandB.h"
int main(int argc, char **argv)
{
ros::init(argc, argv, "talker"); // Initiate new ROS node named "talker"
ros::NodeHandle n;
ros::Publisher chatter_pub = n.advertise<beginner_tutorials::AandB>("chatter", 1000);
ros::Rate loop_rate(10);
int count = 0;
while (ros::ok()) // Keep spinning loop until user presses Ctrl+C
{
beginner_tutorials::AandB msg;
msg.a = 1.0;
msg.b = 2.0;
ROS_INFO("msg a: %.6f, msg b:%.6f", msg.a, msg.b);
chatter_pub.publish(msg);
ros::spinOnce(); // Need to call this function often to allow ROS to process incoming messages
loop_rate.sleep(); // Sleep for the rest of the cycle, to enforce the loop rate
count++;
}
return 0;
}

## Slide 209: CMakeLists.txt

## Slide 210: CMakeLists.txt
cmake_minimum_required(VERSION 2.8.3)
project(beginner_tutorials)
find_package(catkin REQUIRED COMPONENTS
roscpp
rospy
std_msgs
message_generation
)
add_message_files( FILES AandB.msg )
add_service_files ( FILES AddTwoInts.srv )
generate_messages( DEPENDENCIES std_msgs )
catkin_package( CATKIN_DEPENDS roscpp rospy std_msgs message_runtime )
include_directories( ${catkin_INCLUDE_DIRS} )
add_executable(talker src/talker.cpp)
target_link_libraries(talker ${catkin_LIBRARIES})
add_dependencies(talker beginner_tutorials_generate_messages_cpp)

## Slide 211: CMakeLists.txt
cmake_minimum_required(VERSION 2.8.3)
project(beginner_tutorials)
find_package(catkin REQUIRED COMPONENTS
roscpp
rospy
std_msgs
message_generation
)
add_message_files( FILES AandB.msg )
add_service_files ( FILES AddTwoInts.srv )
generate_messages( DEPENDENCIES std_msgs )
catkin_package( CATKIN_DEPENDS roscpp rospy std_msgs message_runtime )
include_directories( ${catkin_INCLUDE_DIRS} )
add_executable(talker src/talker.cpp)
target_link_libraries(talker ${catkin_LIBRARIES})
add_dependencies(talker beginner_tutorials_generate_messages_cpp)
Add the red parts
To CMakeLists.txt

## Slide 212: Building Your Nodes

## Slide 213: Building Your Nodes
Note the bottom line in the CMakeLists file:

## Slide 214: Building Your Nodes
Note the bottom line in the CMakeLists file:
  add_dependencies(talker beginner_tutorials_generate_message_cpp)

## Slide 215: Building Your Nodes
Note the bottom line in the CMakeLists file:
  This makes sure message headers are generated before being used
  add_dependencies(talker beginner_tutorials_generate_message_cpp)

## Slide 216: Building Your Nodes
Note the bottom line in the CMakeLists file:
  This makes sure message headers are generated before being used
After changing the CMakeLists file call catkin_make
  add_dependencies(talker beginner_tutorials_generate_message_cpp)

## Slide 217: Building Your Nodes
Note the bottom line in the CMakeLists file:
  This makes sure message headers are generated before being used
After changing the CMakeLists file call catkin_make
  add_dependencies(talker beginner_tutorials_generate_message_cpp)
  $ cd ~/catkin_ws
  $ catkin_make

## Slide 218: Building Your Nodes
Note the bottom line in the CMakeLists file:
  This makes sure message headers are generated before being used
After changing the CMakeLists file call catkin_make
Or in Eclipse, use short cut “Ctrl + B” to build all packages in the workspace.
  add_dependencies(talker beginner_tutorials_generate_message_cpp)
  $ cd ~/catkin_ws
  $ catkin_make

## Slide 219: Running the Node Inside Eclipse

## Slide 220: Running the Node Inside Eclipse
Create a new launch configuration, by clicking on Run --> Run configurations... --> C/C++ Application (double click or click on New).

## Slide 221: Running the Node Inside Eclipse
Create a new launch configuration, by clicking on Run --> Run configurations... --> C/C++ Application (double click or click on New).
Select the correct binary on the main tab (use the Browse… button)
  ~/catkin_ws/devel/lib/beginner_tutorials/talker

## Slide 222: Running the Node Inside Eclipse
Create a new launch configuration, by clicking on Run --> Run configurations... --> C/C++ Application (double click or click on New).
Select the correct binary on the main tab (use the Browse… button)
  ~/catkin_ws/devel/lib/beginner_tutorials/talker
Make sure roscore is running in a terminal

## Slide 223: Running the Node Inside Eclipse
Create a new launch configuration, by clicking on Run --> Run configurations... --> C/C++ Application (double click or click on New).
Select the correct binary on the main tab (use the Browse… button)
  ~/catkin_ws/devel/lib/beginner_tutorials/talker
Make sure roscore is running in a terminal
Click Run

## Slide 224: Running the Node Inside Eclipse

## Slide 225: Running the Node Inside Eclipse
You could use an ANSI console plugin (e.g. http://www.mihai-nita.net/eclipse/) to get rid of the "[0m" characters in the output.

## Slide 226: Debugging the Node Inside Eclipse
  $ cd ~/catkin_ws/build
  $ cmake ../src -DCMAKE_BUILD_TYPE=Debug
Create a new launch configuration, by clicking on Run--> Debug configurations... --> C/C++ Application (double click or click on New).
Select the correct binary on the main tab (use the Browse… button)
  ~/catkin_ws/devel/lib/beginner_tutorials/talker
Make sure roscore is running in a terminal
Click Debug

## Slide 227: Debugging the Node Inside Eclipse

## Slide 228: Running the Node From Terminal
Make sure you have sourced your workspace's setup.sh file after calling catkin_make:
  Can add this line to your .bashrc startup file
Now you can use rosrun to run your node:
  $ cd ~/catkin_ws
  $ source ./devel/setup.bash
  $ rosrun beginner_tutorials talker

## Slide 229: Running the Node From Terminal

## Slide 230: Examine node talker
  $ rostopic list

## Slide 231: Examine node talker
  $ rostopic echo /chatter

## Slide 232: Learning by Practice
How to customize your own message and service
How to publish a topic
How to subscribe a topic
How to build a server
How to build a client

## Slide 233: Go to eclipse, new source file: listener.cpp, save it Create node listener
#include "ros/ros.h"
#include "beginner_tutorials/AandB.h"
void chatterCallback(const beginner_tutorials::AandB::ConstPtr& msg)
{
ROS_INFO("I heard: msg:a %f, msg:b %f", msg->a, msg->b);
}
int main(int argc, char **argv)
{
ros::init(argc, argv, "listener");
ros::NodeHandle n;
ros::Subscriber sub = n.subscribe("chatter", 1000, chatterCallback);
ros::spin();
return 0;
}

## Slide 234: CMakeLists.txt should look like: CMakeLists.txt

## Slide 235: CMakeLists.txt should look like: CMakeLists.txt
cmake_minimum_required(VERSION 2.8.3)
project(beginner_tutorials)
find_package(catkin REQUIRED COMPONENTS
roscpp
rospy
std_msgs
message_generation
)
add_message_files( FILES AandB.msg )
add_service_files ( FILES AddTwoInts.srv )
generate_messages( DEPENDENCIES std_msgs )
catkin_package( CATKIN_DEPENDS roscpp rospy std_msgs message_runtime )
include_directories( ${catkin_INCLUDE_DIRS} )
add_executable(talker src/talker.cpp)
target_link_libraries(talker ${catkin_LIBRARIES})
add_executable(listener src/listener.cpp)
target_link_libraries(listener ${catkin_LIBRARIES})
add_dependencies(talker beginner_tutorials_generate_messages_cpp)

## Slide 236: CMakeLists.txt should look like: CMakeLists.txt
cmake_minimum_required(VERSION 2.8.3)
project(beginner_tutorials)
find_package(catkin REQUIRED COMPONENTS
roscpp
rospy
std_msgs
message_generation
)
add_message_files( FILES AandB.msg )
add_service_files ( FILES AddTwoInts.srv )
generate_messages( DEPENDENCIES std_msgs )
catkin_package( CATKIN_DEPENDS roscpp rospy std_msgs message_runtime )
include_directories( ${catkin_INCLUDE_DIRS} )
add_executable(talker src/talker.cpp)
target_link_libraries(talker ${catkin_LIBRARIES})
add_executable(listener src/listener.cpp)
target_link_libraries(listener ${catkin_LIBRARIES})
add_dependencies(talker beginner_tutorials_generate_messages_cpp)
Add the red parts
To CMakeLists.txt

## Slide 237: Building node
After changing the CMakeLists file call catkin_make
Or in Eclipse, use short cut “Ctrl + B” to build all packages in the workspace.
  $ cd ~/catkin_ws
  $ catkin_make

## Slide 238: Running node listener
Open another terminal, short cut: Ctrl+Shift+T
  $ rosrun beginner_tutorials listener

## Slide 239: Learning by Practice
How to customize your own message and service
How to publish a topic
How to subscribe a topic
How to build a server
How to build a client

## Slide 240: Go to eclipse, new source file: add_two_ints_server.cpp Create node add_two_ints_server
#include "ros/ros.h"
#include "beginner_tutorials/AddTwoInts.h"
bool add(beginner_tutorials::AddTwoInts::Request &req,
beginner_tutorials::AddTwoInts::Response &res)
{
res.Sum = req.A + req.B;
ROS_INFO("request: x=%ld, y=%ld", (long int)req.A, (long int)req.B);
ROS_INFO("sending back response: [%ld]", (long int)res.Sum);
return true;
}
int main(int argc, char **argv)
{ ros::init(argc, argv, "add_two_ints_server");
ros::NodeHandle n;
ros::ServiceServer service = n.advertiseService("add_two_ints", add);
ROS_INFO("Ready to add two ints.");
ros::spin();
return 0;
}

## Slide 241: CMakeLists.txt should look like: CMakeLists.txt

## Slide 242: CMakeLists.txt should look like: CMakeLists.txt
cmake_minimum_required(VERSION 2.8.3)
project(beginner_tutorials)
find_package(catkin REQUIRED COMPONENTS
roscpp
rospy
std_msgs
message_generation
)
add_message_files( FILES AandB.msg )
add_service_files ( FILES AddTwoInts.srv )
generate_messages( DEPENDENCIES std_msgs )
catkin_package( CATKIN_DEPENDS roscpp rospy std_msgs message_runtime )
include_directories( ${catkin_INCLUDE_DIRS} )
add_executable(talker src/talker.cpp)
target_link_libraries(talker ${catkin_LIBRARIES})
add_executable(listener src/listener.cpp)
target_link_libraries(listener ${catkin_LIBRARIES})
add_executable(add_two_ints_server src/add_two_ints_server.cpp)
target_link_libraries(add_two_ints_server ${catkin_LIBRARIES})
add_dependencies(talker beginner_tutorials_generate_messages_cpp)

## Slide 243: CMakeLists.txt should look like: CMakeLists.txt
cmake_minimum_required(VERSION 2.8.3)
project(beginner_tutorials)
find_package(catkin REQUIRED COMPONENTS
roscpp
rospy
std_msgs
message_generation
)
add_message_files( FILES AandB.msg )
add_service_files ( FILES AddTwoInts.srv )
generate_messages( DEPENDENCIES std_msgs )
catkin_package( CATKIN_DEPENDS roscpp rospy std_msgs message_runtime )
include_directories( ${catkin_INCLUDE_DIRS} )
add_executable(talker src/talker.cpp)
target_link_libraries(talker ${catkin_LIBRARIES})
add_executable(listener src/listener.cpp)
target_link_libraries(listener ${catkin_LIBRARIES})
add_executable(add_two_ints_server src/add_two_ints_server.cpp)
target_link_libraries(add_two_ints_server ${catkin_LIBRARIES})
add_dependencies(talker beginner_tutorials_generate_messages_cpp)
Add the red parts
To CMakeLists.txt

## Slide 244: Building node
After changing the CMakeLists file call catkin_make
Or in Eclipse, use short cut “Ctrl + B” to build all packages in the workspace.
  $ cd ~/catkin_ws
  $ catkin_make

## Slide 245: Running node add_two_ints_server

## Slide 246: Running node add_two_ints_server
Open another terminal, short cut: Ctrl+Shift+T

## Slide 247: Running node add_two_ints_server
Open another terminal, short cut: Ctrl+Shift+T
  $ rosrun beginner_tutorials add_two_ints_server

## Slide 248: Running node add_two_ints_server
Open another terminal, short cut: Ctrl+Shift+T
Open another terminal
  $ rosrun beginner_tutorials add_two_ints_server

## Slide 249: Running node add_two_ints_server
Open another terminal, short cut: Ctrl+Shift+T
Open another terminal
  $ rosrun beginner_tutorials add_two_ints_server
$ rosservice list
$ rosservice args /add_two_ints
$ rosservice call /add_two_ints 1 2

## Slide 250: Learning by Practice
How to customize your own message and service
How to publish a topic
How to subscribe a topic
How to build a server
How to build a client

## Slide 251: Go to eclipse, new source file: add_two_ints_client.cpp Create node add_two_ints_client
#include "ros/ros.h"
#include "beginner_tutorials/AddTwoInts.h"
int main(int argc, char **argv)
{
ros::init(argc, argv, "add_two_ints_client");
if (argc != 3)
{
ROS_INFO("usage: add_two_ints_client X Y");
return 1;
}
ros::NodeHandle n;
ros::ServiceClient client = n.serviceClient<beginner_tutorials::AddTwoInts>("add_two_ints");
beginner_tutorials::AddTwoInts srv;
srv.request.A = atoll(argv[1]);
srv.request.B = atoll(argv[2]);
if (client.call(srv))
{
ROS_INFO("Sum: %ld", (long int)srv.response.Sum);
}
else
{
ROS_ERROR("Failed to call service add_two_ints");
return 1;
}
return 0;
}

## Slide 252: CMakeLists.txt should look like: CMakeLists.txt

## Slide 253: CMakeLists.txt should look like: CMakeLists.txt
cmake_minimum_required(VERSION 2.8.3)
project(beginner_tutorials)
find_package(catkin REQUIRED COMPONENTS
roscpp
rospy
std_msgs
message_generation
)
add_message_files( FILES AandB.msg )
add_service_files ( FILES AddTwoInts.srv )
generate_messages( DEPENDENCIES std_msgs )
catkin_package( CATKIN_DEPENDS roscpp rospy std_msgs message_runtime )
include_directories( ${catkin_INCLUDE_DIRS} )
add_executable(talker src/talker.cpp)
target_link_libraries(talker ${catkin_LIBRARIES})
add_executable(listener src/listener.cpp)
target_link_libraries(listener ${catkin_LIBRARIES})
add_executable(add_two_ints_server src/add_two_ints_server.cpp)
target_link_libraries(add_two_ints_server ${catkin_LIBRARIES})
add_executable(add_two_ints_client src/add_two_ints_client.cpp)
target_link_libraries(add_two_ints_client ${catkin_LIBRARIES})
add_dependencies(talker beginner_tutorials_generate_messages_cpp)

## Slide 254: CMakeLists.txt should look like: CMakeLists.txt
cmake_minimum_required(VERSION 2.8.3)
project(beginner_tutorials)
find_package(catkin REQUIRED COMPONENTS
roscpp
rospy
std_msgs
message_generation
)
add_message_files( FILES AandB.msg )
add_service_files ( FILES AddTwoInts.srv )
generate_messages( DEPENDENCIES std_msgs )
catkin_package( CATKIN_DEPENDS roscpp rospy std_msgs message_runtime )
include_directories( ${catkin_INCLUDE_DIRS} )
add_executable(talker src/talker.cpp)
target_link_libraries(talker ${catkin_LIBRARIES})
add_executable(listener src/listener.cpp)
target_link_libraries(listener ${catkin_LIBRARIES})
add_executable(add_two_ints_server src/add_two_ints_server.cpp)
target_link_libraries(add_two_ints_server ${catkin_LIBRARIES})
add_executable(add_two_ints_client src/add_two_ints_client.cpp)
target_link_libraries(add_two_ints_client ${catkin_LIBRARIES})
add_dependencies(talker beginner_tutorials_generate_messages_cpp)
Add the red parts
To CMakeLists.txt

## Slide 255: Building node
After changing the CMakeLists file call catkin_make
Or in Eclipse, use short cut “Ctrl + B” to build all packages in the workspace.
  $ cd ~/catkin_ws
  $ catkin_make

## Slide 256: Running node add_two_ints_client

## Slide 257: Running node add_two_ints_client
Open another terminal, short cut: Ctrl+Shift+T

## Slide 258: Running node add_two_ints_client
Open another terminal, short cut: Ctrl+Shift+T
  $ rosrun beginner_tutorials add_two_ints_client 1 2

## Slide 259: Running node add_two_ints_client
Open another terminal, short cut: Ctrl+Shift+T
  $ rosrun beginner_tutorials add_two_ints_client 1 2

## Slide 260: roslaunch
•roslaunch is a tool for easily launching multiple ROS nodes, and setting parameters on the Parameter Server.
•It takes in one or more XML configuration files (with the .launch extension) saved in the ‘launch’ folders in packages.
•If roslaunch is used, roscore does not need to be run manually.

## Slide 261: Launch file example
A launch file for launching a node with many parameters
Using <param /> to set parameters
To run a launch file use:
  $ roslaunch package_name file.launch
  $ roslaunch cmd_vel_publisher cmd_vel_publisher.launch
For the above example:

## Slide 262: Launch file example
A launch file for launching two or more nodes simultaneously
Two nodes

## Slide 263: Launch file example
A launch file for launching two or more nodes by including another launch file
Including another launch file

## Slide 264: Retrieving Parameters in c++ file
•There are two methods to retrieve parameters with NodeHandle:
  – getParam(key, output_value)
  – param(key, output_value,default) is similar to getParam(), but allows to specify a default value
•Example: in the cpp file

## Slide 265: Try: Launch
•Use launch file to run two nodes with params
  –Run turtlesim and its velocity control
•Solution:

## Slide 266: Assignment

## Slide 267: Assignment
Create a package that can read keyboard to control the turtle in the turtlesim_node.
Package name: turtle_teleop_key;
Node executable file name: turtle_teleop_key_node;

## Slide 268: Assignment
Create a package that can read keyboard to control the turtle in the turtlesim_node.
Package name: turtle_teleop_key;
Node executable file name: turtle_teleop_key_node;
Hints:
turtlesim_node subscribe a topic called /turtle1/cmd_vel.
what is the type of this topic?
(rostopic type /turtle1/cmd_vel) and
(rosmsg show geometry_msgs/Twist)

## Slide 269: Reference and Code
Books
ROS By Example for Hydro Volume 1
(http://yunpan.cn/cwbkvHTRcifF7 Password:b936)
ROS basic; Navigation; Speech Recognition; Vision;
……
ROS By Example for Hydro Volume 2
(http://yunpan.cn/cwbkpDVuVk3mG Password:d23a)
Robot Model Creation; Dynamic Parameters; 3D Tracking;
3D Simulation; MoveIt!;
……
Code
https://github.com/pirobot/rbx1/tree/indigo-devel
https://github.com/pirobot/rbx2/tree/indigo-devel

## Slide 270: Other Materials
1. ROS Cheat Sheets
http://yunpan.cn/cwUDTFWgemTW5 Password: b775
2. Linux Command Reference:
http://yunpan.cn/cwUzgtkk84NyB Password: 514b

## Slide 271
Thank you!